## Slide 1
StevensWater
“SmartPT”
SDI-12
Sampler
Switched 12V
RS-485 MODBUS
RS-232
MODBUS
Sigma 950
flowmeter
The Sutron Universe
PSA-AV
sensor
Sensor | Level | Velocity | Comm
PSA-AV | ✓ (PT) | ✓ | RS-485
Sigma 950 | ✓ (bubbler) | ✓ | RS-232
Stevens PT | ✓ (PT) | HvF table | SDI-12
OTT | ✓ (bubbler) | HvF table | SDI-12
OTT Bubbler
Cell modem to
Phone, PC, server

## Slide 2
StevensWater
“SmartPT”
Sampler
Sigma 950
flowmeter
The Sutron Universe
PSA-AV
sensor
Sensor | Level | Velocity | Price
PSA-AV | ✓ (PT) | ✓ | $2,200
Sigma 950 | ✓ (bubbler) | ✓ | Priceless
Stevens PT | ✓ (PT) | HvF table | $800
OTT | ✓ (bubbler) | HvF table | $2,800
OTT Bubbler
Cell modem to
Phone, PC, server
$10-20/month
$1,600
$100
$300
$1,000-3,000
Item | Cost
Sutron | $1,600
Flow | $800 – $3k
Sampler | $1k - $3k
Power | $100-400
Telemetry | $120-240/yr
Enclosure | $100-300
Total | $4k – $8k
$2,200
$800
$2,800
Priceless

## Slide 3
StevensWater
“SmartPT”
Sampler
Sigma 950
flowmeter
The Sutron Universe
PSA-AV
sensor
Item | Connection | Price
Battery cable, ring terminals | 2 strand, 16 ga | $25-50
Solar Panel | Bare wires, usually part of solar panel | $0-100
PSA-AV sensor | Bulgin 9 pin female Wire | $30
Sampler | Sampler comm cable (cut to bare wire) | $227 / 2
Sigma 950 | Hach data download Male/male adapter | $95 $3
Antenna | SMA | $50-75
OTT Bubbler
Battery cable
Additional cables and connectors needed
Bulgin 9pin plug
“road dot” antenna
Standard antenna
Hach sampler control cable
Hach data download cable
w/male male adapter
Flying leads

## Slide 4
ISCO 3700
Sampler
Hach sampler
control cable
ISCO Signature
flowmeter
Sensor | Comm | $$
Signature | RS-485 | NA
3700 Sampler | V pulse | NA
Sutron Xlink |  | $1,600
Cell data plan |  | $150/yr
Antenna w/cable |  | $300
Sampler control cable |  | $250
Enclosure |  | $200
Power Supply |  | $50
Total: |  | $2,400 +cell plan
Cell modem to
Phone, PC, server
RS-485
MODBUS
Cellular antenna
Enclosure
AC to DC power supply